## Slide 1
REVIEW PRESENTATION • COMPUTER ARCHITECTURE
BIT MANIPULATION
in Assembly Language
How programs read, set, and transform individual bits at the hardware level — and why it still matters.
01001010 01000010 01010100 01000011 01001111 01000100 01000101

## Slide 2
Why Bit Manipulation Matters
The bit is the atomic unit of digital information
Bit manipulation is the direct inspection, setting, clearing, and transformation of individual bits within a machine word.
It has been central to programming since the earliest computers, when scarce memory made packing information into individual bits a practical necessity.
Even as high-level languages introduced booleans, structs, and flags, assembly-level bit manipulation persisted — remaining essential wherever performance, memory footprint, or direct hardware access matter most.
Performance
Single-instruction bitwise operations avoid costly arithmetic and branching.
Memory Efficiency
Packing flags and fields into individual bits conserves scarce storage.
Hardware Control
Peripheral and register configuration is expressed directly as bit patterns.
02
Bit Manipulation in Assembly Language

## Slide 3
Fundamental Bitwise Operations
Four logical operations, plus shifts and rotates, underlie every technique
Logical Operations
A | B | AND | OR | XOR | NOT A
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
AND sets a bit only where both operands are 1 — used to clear or mask bits.
OR sets a bit where either operand is 1 — used to set bits.
XOR sets a bit where operands differ — used to toggle bits.
Shifts & Rotates
SHL / LSL
Shift left, fill with 0 — multiply by 2 per position.
SHR / LSR
Shift right (logical), fill with 0.
SAR / ASR
Shift right, filling with the sign bit — signed divide by 2.
ROL / ROR
Circular shift — bits leaving one end re-enter the other.
03
Bit Manipulation in Assembly Language

## Slide 4
Assembly Instructions: x86 vs. ARM
Shared logical primitives, different approaches to bit fields
x86 (Intel / AMD)
AND · OR · XOR · NOT
Core logical operations
SHL · SHR · SAR
Logical and arithmetic shifts
ROL · ROR · RCL · RCR
Rotate, with/without carry
BT · BTS · BTR · BTC
Test / set / reset / complement a bit
BSF · BSR
Find lowest / highest set bit
POPCNT · TZCNT · LZCNT
Hardware-accelerated bit counting
ARM (AArch32 / AArch64)
AND · ORR · EOR · MVN
Core logical operations
LSL · LSR · ASR · ROR
Shift and rotate
BFI · BFC
Insert / clear a bit field in one step
UBFX · SBFX
Extract a bit field, unsigned / signed
CLZ
Count leading zeros
RBIT
Reverse bit order in one instruction
04
Bit Manipulation in Assembly Language

## Slide 5
Worked Example: Counting Set Bits
Kernighan's algorithm: n & (n − 1) clears the lowest set bit each step
Step | n (before) | n AND (n−1)
1 | 1011 0110 | 1011 0100
2 | 1011 0100 | 1011 0000
3 | 1011 0000 | 1010 0000
4 | 1010 0000 | 1000 0000
5 | 1000 0000 | 0000 0000
Each iteration clears the least-significant set bit of n, so the number of iterations needed to reach zero equals the number of 1-bits originally present — an algorithm whose cost depends on data content, not word width.
5
SET BITS
in 1011 0110 (0xB6, decimal 182)
On processors with SSE4.2, this entire result is produced in one cycle by POPCNT.
05
Bit Manipulation in Assembly Language

## Slide 6
Real-World Applications
Bit-level efficiency still underlies performance-critical software
Cryptography
Bit permutations and XOR-based key mixing secure ciphers such as AES and DES.
Graphics
Masking and shifting pack RGB(A) color channels into a single pixel word.
Embedded Systems
Setting/clearing register bits configures timers, GPIO, and peripherals.
Networking
Header flags, offsets, and checksums rely on bitwise parsing.
OS Kernels
Page-table flags and atomic bit-test-and-set enable synchronization.
Data Compression
Huffman coding and run-length flags depend on precise bit packing.
06
Bit Manipulation in Assembly Language

## Slide 7
Key Takeaways
Four logical operations — AND, OR, XOR, NOT — combined with shifts and rotates, form the basis of every bit-manipulation technique.
x86 and ARM expose these operations through dedicated instructions, and modern extensions (BMI2, RISC-V “B”) add hardware acceleration.
Masking idioms — set, clear, toggle, test, extract — remain foundational to compiler intrinsics and high-level bitwise code alike.
From cryptography to embedded systems, efficient bit manipulation continues to underlie performance-critical software.
Thank you